## Slide 1
Microstore
512x32 ROM
MIR
32
ALU
16MB x 32
RAM
32
32
32
MAR
24
MPC
9
MDR
32
0
1
3
AC
SP
ZM
PC
XM
YM
IR
CT
CY
A
B
000: A
001:~A
010:A&B
011:A*B
100:A+B
101:A-B
110:SL
111:SR
BP
MB
RD
WR
CND
2
9
S
Z
C
DC
F
MODE
TTB
ITB
INTE
TMP
INTX
TMP
TMP
Timer

## Slide 2
C
A
B
ALU
MAR
RD
WR
CND
ADDR
Micro Instruction Format
5
5
5
3
1
1
1
2
9
000: A
001:~A
010:A&B
011:A*B
100:A+B
101:A-B
110:Shift Left
111:Shift Right
ALU:

## Slide 3
Opcode | Form | Name | Description
0x00 | LD X | Load | AC = MEM[x]
0x01 | ST X | Store | MEM[x] = AC
0x02 | ADD X | Add | AC = AC + MEM[x]; CY=carry
0x03 | SUB X | Subtract | AC = AC – MEM[x]
0x04 | LDR S | Load Relative | AC = MEM[BP + S]
0x05 | STR S | Store Relative | MEM[BP + S] = AC
0x06 | ADDR S | Add Relative | AC = AC + MEM[BP + S]; CY=carry
0x07 | SUBR S | Subtract Relative | AC = AC – MEM[BP + S]
0x08 | LDC X | Load Constant | AC = X
0x09 | JA X | Jump Always | PC = X
0x0A | JZOP X | Jump Zero or Positive | If(AC >= 0) PC = X
0x0B | JN X | Jump Negative | If(AC < 0) PC = X
0x0C | JZ X | Jump Zero | If(AC==0) PC = X
0x0D | JNZ X | Jump Non-Zero | If(AC!=0) PC = X
0x0E | CALL X | Call Procedure | MEM[--SP] = PC; PC = X
0x0F | RET | Return | PC = MEM[SP++]

## Slide 4
Opcode | Form | Name | Description
0x10 | LDI | Load Indirect | AC = MEM[AC]
0x11 | STI | Store Indirect | MEM[AC] = MEM[SP++]
0x12 | PUSH | Push | MEM[--SP] = AC
0x13 | POP | Pop | AC = MEM[SP++]
0x14 | ALOC X | Allocate | SP = SP - X
0x15 | DLOC X | Deallocate | SP = SP + X
0x16 | SWAP | Swap | TMP = AC; AC = SP; SP = TMP
0x17 | ADDC X | Add Constant | AC = AC + X
0x18 | SUBC X | Subtract Constant | AC = AC - X
0x19 | ESBA | Establish Base Address | MEM[--SP] = BP; BP = SP
0x1A | REBA | Restore Base Address | SP = BP; BP = MEM[SP++]
0x1B | CORA | Convert Relative Address | AC = AC + BP
0x1C | SCMP X | Signed Compare | TMP=AC-MEM[X];AC=-1¦0¦1
0x1D | UCMP X | Unsigned Compare | TMP=AC-MEM[X];AC=-1¦0¦1
0x1E | SHLL X | Shift Left Logical | AC = AC << X (inject 0’s)
0x1F | SHRL X | Shift Right Logical | AC = AC >> X (inject 0’s)

## Slide 5
Opcode | Form | Name | Description
0x20 | SHRA | Shift Right Arith | AC = AC >> Z (inject sign)
0x21 | MULS | Multiply (shift-add) | AC = AC * MEM[X]
0x22 | MULT | Multiply (hardware) | AC = AC * MEM[X]
0x23 | DIV X | Divide | AC = AC / MEM[X]
0x24 | REM X | Remainder | AC = AC % MEM[X]
0x25 | ADDY X | Add with carry | AC = AC + MEM[X] + CY;CY = carry
0x26 | OR X | bitwise or | AC = AC ¦ MEM[X]
0x27 | XOR X | Bitwise exclusive or | AC = AC Ꚛ MEM[X]
0x28 | AND X | Bitwise and | AC = AC & MEM[X]
0x29 | FLIP | Bitwise complement | AC = ~AC
0x2A | CALI | Call indirect | MEM[SP--] = PC;PC = AC
0x2B | SECT X | Set count register | CT = X
0x2C | DECT | Decrement count register | CT = CT – 1; if(CT==0)PC=PC+1
0x2D | SODD | Skip on odd | If(AC%2==1)PC=PC+1
0x2E | BPBP | BP to BP | BP=MEM[BP]
0x2F | POBP | Pop BP | BP=MEM[SP++]

## Slide 6
Opcode | Form | Name | Description
0x30 | PUBP | Push BP | MEM[--SP]=BP
0x31 | BCPY | Block Copy | TEMP=MEM[SP++]while(CT--) { MEM[AC++]=MEM[TEMP++] }
0x32 | SYSC X | System Call | MEM[--SP]=PC;MODE=0;PC = MEM[TTB+X];
0x33 | EXIT X | Exit | AC=X; exit program
0x34 | ITTB X | Initialize Trap Table | (PRIV) TTB = X
0x35 | IITB X | Initialize Interrupt Table | (PRIV) ITB = X
0x36 | ENBI | Enable Interrupts | (PRIV)INTE=1
0x37 | DISI | Disable Interrupts | (PRIV)INTE=0
0x38 | HNDI | Handle Interrupt | (PRIV)PC=MEM[ITT+INTX];
0x39 |  |  | 
0x3A |  |  | 
0x3B |  |  | 
03C |  |  | 
0x3D |  |  | 
0x3E |  |  | 
0x3F |  |  |